## Slide 1
Instruction Execution Cycle and CPU Performance
CSA1221-Computer Architecture
PRESENTED BY
MUTHUPRIYA R
(192421002)
GUIDED BY
Dr. VIJAYA BHASKAR K

## Slide 2
INTRODUCTION
What is the Instruction Execution Cycle?
The Instruction Execution Cycle is the process the CPU follows to execute a program.
It consists of three main stages:
  Fetch
  Decode
  Execute
This cycle repeats until all program instructions are completed.

## Slide 3
Program in Memory
Fetch Instruction
Decode Instruction
Execute Instruction
Store Result
Next Instruction
WORKFLOW

## Slide 4
FETCH STAGE
Program Counter (PC) stores the address of the next instruction.
Address is sent to memory.
Instruction is fetched into the Instruction Register (IR).
PC is updated to the next instruction.
Example: Memory Address: 2000
Instruction: ADD R1, R2

## Slide 5
DECODE AND EXECUTE
Decode
Control Unit interprets the instruction.
Determines required operation.
Identifies operands.
Execute
ALU performs arithmetic or logical operation.
Result is stored in a register or memory.
Example Instruction :ADD R1,R2
If
R1 = 10, R2 = 5
Result: R1 = 15

## Slide 6
CPU PERFORMANCE METRICS
1. Clock Cycle
Smallest unit of CPU operation.
Measured in GHz.
2. CPI (Cycles Per Instruction)
Average number of clock cycles needed for one instruction.
Formula: CPI = Total Clock Cycles
Total Instructions
3. Execution Time
Execution Time = Instruction Count × CPI × Clock Cycle Time

## Slide 7
EFFECT OF INEFFICIENCIES
STAGE | PROBLEM | EFFECT
Fetch | Slow memory | CPU waits longer
Decode | Complex instruction | More decoding time
Execute | Slow ALU or cache miss | Higher execution time

## Slide 8
CONCLUSION
CPU executes instructions using Fetch → Decode → Execute.
CPU performance depends on:
  Clock Cycles
  CPI
  Execution Time
Reducing delays in any stage improves system performance.
Efficient instruction execution leads to faster program execution.
An optimized instruction execution cycle improves CPU efficiency, reduces execution time, and enhances overall computer system performance.

## Slide 9
THANKYOU